## Slide 1
2024 Deep Learning
Hardware Design Competition:
Final Presentation
Dongmin Han, Changwoo Lee, Donghwee Son
ChipChamps, Seoul National University

## Slide 2
Contents
Outline
Idea and Novelty
Hardware Design
Team Plan
Others

## Slide 3
1. Outline
Objective
  Appropriately quantize the model so that all computations can be done in integer, without significant accuracy loss.
  Design CNN inference accelerator considering accuracy, time, power, and resource utilization.
  Implement the designed modules on actual HW, like FPGA.

## Slide 4
1. Outline
Final Result
  Quantization (mAP) : 81.10%

## Slide 5
1. Outline
Final Result
  Simulation completed for all layers (conv0 ~ conv20)
    This was implemented only with regs, and assuming all ifmaps/weights for each layer can fit into the regs. (Impractical on HW)
    Therefore, ifmap tiling was implemented to put practical sizes of data can fit into the limited reg/bram of FPGA.

## Slide 6
2. Idea and Novelty: Quantization Method
Weight Distribution
  Overall layer-wise view
  Min/Max ranges are quite limited!

## Slide 7
2. Idea and Novelty: Quantization Method
Weight Distribution
  Extracted weight values to get the best scaling factor empirically
Layer 0
Layer 2
Layer 4
Layer 14
Layer 17
Layer 20

## Slide 8
2. Idea and Novelty: Quantization Method
Weight Distribution
  From this result, get best scaling factor which minimizes our metric: Mean Squared Error (MSE)[1]
  Also, we observed distribution mean and accepted symmetric scheme
gives
quantization
standpoints
MSE=0.919
MSE=0.00031
[1] Minsik Kim, Kyoungseok Oh, Youngmock Cho, Hojin Seo, Xuan Truong Nguyen, and Hyuk-Jae Lee. 2024. A Low-Latency FPGA Accelerator for YOLOv3-Tiny With Flexible Layerwise Mapping and Dataflow. IEEE Transactions on Circuits and Systems I: Regular Papers 71, 3 (2024), 1158-1171. DOI:https://doi.org/10.1109/tcsi.2023.3335949

## Slide 9
2. Idea and Novelty: Quantization Method
Power-of-two quantizer
  In the previous setting, we measure MSE of only by power-of-two
  This choice can bring hardware efficiencies as scaling with s corresponds to simple bit-shift
  The restricted expressiveness of the scale factor can complicate the trade-off between the rounding and clipping error

## Slide 10
Quantization granularity
  Quantization parameters can be set per layer, per channel, … this is called quantization granularity
  Our parameters are shared per layer, for the sake of simplicity and hardware efficiency
2. Idea and Novelty: Quantization Method

## Slide 11
2. Idea and Novelty: CONV Layers
Three distinct computation methods each for CONV00, 3x3, and 1x1 conv.
  CONV00
    The only layer with ifmap channel of 3.
    Needs separate dataflow compared to ordinary 3x3 convolution.

## Slide 12
2. Idea and Novelty: CONV Layers
Three distinct computation methods each for CONV00, 3x3, and 1x1 conv.
  3x3 convolution (except CONV00)
    All ifmap and ofmap channels are multiple of 16.
    All layers except CONV13 are followed by ReLU and maxpool.
    → Integrated!

## Slide 13
2. Idea and Novelty: CONV Layers
Three distinct computation methods each for CONV00, 3x3, and 1x1 conv.
  1x1 convolution
    All layers except CONV14 and CONV20 have ofmap channels with multiple of 16.
    All layers except CONV14 and CONV20 are followed with ReLU.
    No maxpool!

## Slide 14
3. Hardware Design
  Terminology
  Ni: ifmap channel dimension
  No: ofmap channel dimension
  Fx, Fy: filter dimension
  Tr: row-wise factor, always set to 2
  Tc: column-wise factor, always set to 2
  Ti: ifmap channel-wise factor
  To: ofmap channel-wise factor
  CONV module consumes (Tr x Tc) x (Fx x Fy x Ti) ifmap pixels and produces (Tr x Tc x To) ofmap pixels every cycle!

## Slide 15
3. Hardware Design
PE utilization
  Total 4 mac_arrays
    Each mac_array contains 9 mac_modules
      Each mac_module contains 16 multipliers and an adder_tree
  Total 4 x 9 x 16 = 576 multipliers!
    Nexys A7-100T FPGA board contains 240 DSPs which can map to 480 multipliers.
    Remaining 96 multipliers are mapped to LUTs.

## Slide 16
3. Hardware Design
mac_array
mac16
Total 9 mac_modules.
Last mac utilized for 3x3 CONV only!
+
MUX
1x1x4
layer 0
1x1x8
conv 1x1
+
conv 3x3
1x1x1
IFM
Weight
OFM
conv mode

## Slide 17
3. Hardware Design: CONV00
CONV00 parameters:
  Ni = 4 (actually 3)
  No = 16
  Fx, Fy = 3
  Tr, Tc = 2
  Ti, To = 4

## Slide 18
3. Hardware Design: CONV00
Data Processing of CONV00
  Every cycle, consumes 4x4x3 IFM (window) and produces 2x2x4 OFM
  Each mac_array using 8 mac_modules, and 2 mac_modules working as a pair to process 3x3x3 ifm!
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 3x3x3 ifm in 4x4x3 window
1x1x4
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
256 x 256 x 3
256 x 256 x 16
3x3x3x4 weight replicated in each mac_array
3x3x3
1x1x4
paired mac_modules

## Slide 19
3. Hardware Design: CONV00
PE utilization of CONV00
  3x3x3x4 = 108 computations done in each mac_array
  mac_array has 16x9 = 144 multipliers
  PE utilization = 108/144 = 75%
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 3x3x3 ifm in 4x4x3 window
1x1x4
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
256 x 256 x 3
256 x 256 x 16
3x3x3x4 weight replicated in each mac_array
3x3x3
1x1x4
paired mac_modules

## Slide 20
3. Hardware Design: CONV00
mac_array
mac16
Total 9 mac_modules.
Last mac utilized for 3x3 CONV only!
+
MUX
1x1x4
layer 0
1x1x8
conv 1x1
+
conv 3x3
1x1x1
IFM
Weight
OFM
conv mode

## Slide 21
RTL simulation result exactly matches
the compiled result of C code!
(CONV00_output.hex)
-> Accuracy confirmed!
3. Hardware Design: CONV00 (This slide needs modification)

## Slide 22
3. Hardware Design: 3x3 conv
3x3 conv parameters:
  Fx, Fy = 3
  Tr, Tc = 2
  Ti = 16
  To = 1

## Slide 23
3. Hardware Design: 3x3 conv
Data Processing of 3x3 conv
  Every cycle, consumes 4x4x16 IFM (window) and produces 2x2x1 OFM
  Each mac_array using 9 mac_modules, and the whole dot product results are summed up to produce 1x1x1 output
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 3x3x16 ifm in 4x4x16 window
1x1x1
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
H x W x Ni
H x W x No
3x3x16x1 weight replicated in each mac_array
3x3x16
1x1x1
MAC16
9 mac_modules

## Slide 24
3. Hardware Design: 3x3 conv
PE utilization of 3x3 conv
  3x3x16x1 = 144 computations done in each mac_array
  mac_array has 16x9 = 144 multipliers
  PE utilization = 144/144 = 100%
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 3x3x16 ifm in 4x4x16 window
1x1x1
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
H x W x Ni
H x W x No
3x3x16x1 weight replicated in each mac_array
3x3x16
1x1x1
MAC16
9 mac_modules

## Slide 25
3. Hardware Design: 3x3 conv
mac_array
mac16
Total 9 mac_modules.
Last mac utilized for 3x3 CONV only!
+
MUX
1x1x4
layer 0
1x1x8
conv 1x1
+
conv 3x3
1x1x1
IFM
Weight
OFM
conv mode

## Slide 26
3. Hardware Design: 3x3 conv
For CONV00 and 3x3 conv, all layers except CONV13 are followed by ReLU and maxpool.
Bias addition, ReLU, quantization for the next layer, and maxpool operations are all integrated at the outputs of each mac_arrays!
No additional module, all operations can be done in 1 cycle.

## Slide 27
3. Hardware Design: 3x3 conv
실행 화면 필요 !!!

## Slide 28
3. Hardware Design: 1x1 conv
1x1 conv parameters:
  Fx, Fy = 1
  Tr, Tc = 2
  Ti = 16
  To = 8

## Slide 29
3. Hardware Design: 1x1 conv
Data Processing of 1x1 conv
  Every cycle, consumes 2x2x16 IFM (window) and produces 2x2x8 OFM
  Each mac_array using 8 mac_modules, each processing 1x1x16 dot product!
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 1x1x16 ifm in 2x2x16 window
1x1x8
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
H x W x Ni
H x W x No
1x1x16x8 weight replicated in each mac_array
1x1x16
1x1x8

## Slide 30
3. Hardware Design: 1x1 conv
PE utilization of 1x1 conv
  1x1x16x8 = 128 computations done in each mac_array
  mac_array has 16x9 = 144 multipliers
  PE utilization = 128/144 = 88.9%
IFM
OFM
MAC
Array
MAC
Array
MAC
Array
four 1x1x16 ifm in 2x2x16 window
1x1x8
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC16
MAC
Array
H x W x Ni
H x W x No
1x1x16x8 weight replicated in each mac_array
1x1x16
1x1x8

## Slide 31
3. Hardware Design: 1x1 conv
mac_array
mac16
Total 9 mac_modules.
Last mac utilized for 3x3 CONV only!
+
MUX
1x1x4
layer 0
1x1x8
conv 1x1
+
conv 3x3
1x1x1
IFM
Weight
OFM
conv mode

## Slide 32
3. Hardware Design: 1x1 conv
실행 화면 필요 !!!

## Slide 33
1. 개요
구현 결과
  Quantization (mAP)
  H/W inference results (@XXXMHz)
  Board implementation
    Power
    LUT
    BRAM
    DSP
Capture images

## Slide 34
2. 아이디어 및 차별성
Concept 1: …

## Slide 35
3. 설계 세부내용
Proposed block diagram

## Slide 36
3. 설계 세부내용
BRAM configuration …

## Slide 37
4. 일정 계획 및 추진방법
추진 일정 및 방법
  업무 분장: Algorithm 구현 및 평가 / H/W 설계 및 FPGA 구현 / Test Bench 설계 및 검증
Category | Item | February |  |  |  | March |  |  |  |  | April |  |  |  | May |  |  | 
 |  | w1 | w2 | w3 | w4 | w1 | w2 | w3 | w4 | w5 | w1 | w2 | w3 | w4 | w1 | w2 | w3 | w4
Study | 가속기 관련 논문 Study |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Algorithm 구현 및 평가 | Quantization방법 결정 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | quantization 구현 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Data Reordering |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Test Bench 설계 및 검증 | single/multi layer TB |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | TB update w/ fixed C-model |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
H/W 설계 및 FPGA 구현 | Block Diagram 작성 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | Shared global buffer feasibility 확인 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | RTL 설계 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | RTL 검증 및 FPGA 최적화 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 38
5. 기타사항
Any issue

## Slide 39
Outline
Background
Page setup
Fonts and colors
General guideline for good slides
Text and figures
Saving and bringing your file

## Slide 40
Page setup
Set up the slide for Wide screen(16:9).
Do not use A4 or 35mm slide.
Take 5mm for top, bottom, right and left margins.
All pages should be in horizontal (landscape) format, not vertical.
No logos are permitted except on the title page.
Put page number in the bottom right.

## Slide 41
Fonts
Use Arial or Helvetica font in bold type.
  Use sans-serif fonts. Don’t use serif fonts, which project poorly.
  ex. Times New Roman, Century.
  Use 24 points or larger.
  Anything less than 20 points is too small (e.g. 18 point).
  Think about the audience watching your presentation from the back of a large ballroom.
You have to be innovative to limit and reconfigure the contents of a slide to increase the font size.

## Slide 42
Colors
All backgrounds must be white with no pattern.
Basically text must be in black.
Color may be used only when it adds clarity of the presentation.
Use colors with good contrast.
Reds and blues are OK. Avoid yellows and light colors, except as a local background in a boxed area.

## Slide 43
Example: color and font choices
This text is clear and standard
but if your font is too thin, it won’t be visible.
This combination has good contrast.
This 18-points text is too small.
This combination will be impossible to see - no contrast.
This combination is not suitable for color-vision deficient people.

## Slide 44
General guideline
Keep concepts as simple as possible.
Limit each page to one main idea.
Use several simple figures rather than one complex one.
Make duplicate copies of a page if you plan to refer to it more than once.
Do not plan to go back to a slide.
Rehearse your talk aloud in front of colleagues.

## Slide 45
Text slides
Don’t use a lengthy sentence. Use a short phrase and a simple sentence.
  - Explain with sentences verbally but don’t write the sentences on a slide.
Use no more than 10 lines of text per page.

## Slide 46
Graphs and figures
Use a minimum line width of 2 points for all lines in drawings.
Fonts embedded in figures should also comply with a guideline for text.
Often, graphical data imported from other programs will have
small fonts & thin lines.
  - Completely redraw if you can’t fix this.

## Slide 47
Example of a good figure
Simple graph, thick, bold axes, large fonts
0.0
0.5
1.0
1.5
0
1
2
3
4
5
Delay (ps)
Power (µW)
Case 1
Case 2
Case 3

## Slide 48
Example of a bad figure
Fonts & lines too small
Colors difficult to read

## Slide 49
Saving your file
Save your file with the following format
  “AIX2023_(Team Name).pptx(.pdf)“

## Slide 50
Uploading your presentation
Please submit your slide file with your video file
Bring the slide file to the conference using a USB memory.
Read associated documents for important dates and our program.

## Slide 51
Video Guideline
Slide Format: 16:9
Recommended Encoding Settings:
Format: MP4
Compression: H.264 (AAC for Audio)
Resolution: Minimum height of 480 pixels
Frame Rate: Content should be encoded and uploaded in the same frame rate it was recorded. Common frame rates include: 24, 25, 30, 48, 50, 60 fps
Bitrate: Variable
File Size:
10 minutes: 150 MB or less

## Slide 52
Video Guideline
File Naming Convention:
Videos should be named AIX2024_(TeamName).mp4
Duration
Lecture: 10 min.
Note: The above Duration is for pre-recording your presentation video, excluding the Q&A time during the real-time presentation